## Slide 1: Cyber Seeds for Superfast Engineering Design
Professor Mark Price
Professor of Aeronautics, Queen’s University Belfast, Mechanical and Aerospace Engineering
EPSRC Fellow in Engineering Design
A presentation for the Northern Ireland Science Festival 2026
Innovation in Action: Engineering Research Showcase 13th February 2026

## Slide 3
Note the AI generated text!
So many spelling mistakes!!!
Design is:
  the process of using creativity to solve problems and shape ideas into practical solutions
  (The Design Council)

## Slide 4
4 million parts
1500 companies
30 countries
Airbus A380

## Slide 5
Isaac Newton
Charles Darwin

## Slide 6
At the core of all this is DNA - the genes of life itself!
These are the instructions for how every plant and animal on the planet grows and develops into a living organism.

## Slide 10
Organism
normal
centroid
Cell1
Cell3
Cell4
Cell2
Initialise Cell Zero
Development
Initialise Organism
Generative Design Tools

## Slide 12
Start with a ‘seed’ – i.e. concept zero
Gene Regulatory Network represented by an Artificial Neural Network (ANN)
Each cell has a set of genes i.e. its own gene regulatory network
Environment includes:
Loads
Constraints
Stress
Deflections
Symmetry
Objectives
Mass
Cost
Schedule
Each triangle is a cell

## Slide 13
Explore lots of solutions…
Includes constraints, can include symmetry or shape and mass.

## Slide 14
2D Pressure plates
2D Thermal Stresses
19:13:20
HFL*: 2.739
Vol: 6820
2D Heat Convection
2D Heat Conduction

## Slide 15: Curved Plate 1
High Temp
Low Temp
Objective:
Manage Heat across the plate
Network (RNEAT)
Input: Face Heat Flux
Output: Fin Addition

## Slide 17: Pareto
Fins develop and dissipate heat at key region
Run for 100 generations:
225 mins

## Slide 19
14-8
Best Compromise between heat flux and structural mass.
NB fins are represented as triangular facets here but can be any shape in the real concept.
Evolution takes 45 minutes for 20 gens
Or 225 minutes for 100 gens.
Seed
Just plant the seed & grow the solution directly – no evolution!
Superfast seed takes 5.4 seconds!
Speed up of 2,500 times
3 orders of magnitude.

## Slide 20: Wing

## Slide 21: Wing Box Problem Outline
Use RIED software to evolve a range of viable wing box design solutions for the Airbus “City Airbus”.
Small aircraft to carry 4 people, total load of 2000kg (~20kN)
Wing-span of 8m (conventional wing)
NACA0020 aerofoil profile (equation-driven and symmetric)
Target weight: 100kg
Semi-span = 4m

## Slide 22: How is the “state” assessed?
G: Global RIED Response
L: Local RIED Response
Specification
Critical Buckling Load
[Buckling Analysis G]
Weight G
Material cost
Machining cost
Assembly cost
Manufacturing Cost
[Cost Model – Next Slide G]
Wing Lift / Drag
[Look-up Tables G]
Deflection
[Static Analysis G]
Stress
[Static AnalysisG,L]
Elevated stress should lead to GRN promote thickening in this region

## Slide 23
Speed up using superfast cyber seed is ~600
~2 days down to 5 minutes
i.e. 2 orders of magnitude!!

## Slide 24: Trailer Design Challenge with AMIC NB AMIC is Norther Ireland’s Advanced Manufacturing Innovation Centre

## Slide 25: Project Brief
Create demonstration seedling for the design of a Trailer Chassis using the RIED Engine
  Phase 1: Conventional Design Process
  Phase 2: RIED Design Process
high degree of customisation in trailer market

## Slide 26: Final CAD Geometry

## Slide 27: Automated CAD Generation of Trailer Seedling Workflow
Chassis members are mirrored
Plane created at ymax (top face trailer bed) and nodes joined (based on the applied force nodes from RIED GUI) in a 3rd sketch
Structural Designer creates members for the lines in 3rd sketch
Trailer bed generated based on outer extents of the chassis frame
Leaf spring generated based on trailer load and number of axles to calculate number of leaves
COTS sub-assembly created with positional relationship for u-bolt plate to spring connection based on number of leaves

## Slide 28: Automated CAD Generation of Trailer Seedling Workflow
Trailer frame and bed are joined with the COTS sub-assembly
*Equaliser and second set of axle, wheels, springs and brackets inserted when using dual-axle option

## Slide 29: Demonstration of quick cost studies
Approximate cut-lists, weights, and costs and BoM’s generated for all 600 designs in just 35 seconds

## Slide 30: Automated Generation of Quotation Document Workflow
Right click on a result
Identify Result Directory
Parse geometry results files for cross-sections, volumes, and elements lengths
Parse inputs file for design constraint data
CAD preview images appended to .pdf
Compile and add in-house and COTS component costs

## Slide 31: Overview of Quotation Document Results
 |  | Quotation Turn Around Time
Double Axle (Conventional) |  | 1-2 weeks
Single Axle (RIED) |  | Less than 3 minutes
Double Axle (RIED) |  | Less than 3 minutes
With approx. 6 months development time, only about 12 quotations is break even!
Speed up per quote is ~6,000
i.e. 3 orders of magnitude!!

## Slide 32
Chris Bosse, co-director of the Australian architecture agency Lava (Laboratory for Visionary Architecture).
The designs often appear similar to shapes and structures found in the natural world (Credit: Airbus) Ref bbc.co.uk/future

## Slide 33
And remember…….
Imagination is the only weapon in the war against reality.” ― Lewis Carroll, Alice in Wonderland

## Slide 34: Thank You!